## Slide 1: BIRLA VISWAKARMA MAHAVIDHYALAYA VALLABHVIDHYANAGAR(007),ANAND
PREPARED BY:
GAURAV JINDAL-130070107025
ANKUR KIYADA-130070107029
ABHISHEK MEHTA - 130070107031
SUBJECT : MICROPROCESSOR ARCH. & INTERFACE
TOPIC:WRITE A ALP THAT SHOWS STRING CONTAINS GIVEN SUBSTRING OR NOT.
DEPEARTMENT OF COMPUTER

## Slide 2: Problem Statement :
You are given 10 bytes, stored in memory locations, starting from 9100H,of which represent ASCII values of certain alphabets.
Write an ALP, to find if ‘abc’ is a substring of the given string, stored at 9100H onwards.
If so, the program should write 01H at 9200H memory locations.
If NO, the program should write 00H at 9200H memory locations.

## Slide 3: Program:
MEMORY LOCATION | HEX. CODE | LABEL | MNEMONIC | OPERAND | COMMENT
4200H | 0E |  | MVI | C,10 | ;Loading C with no of inputs to use as a counter
4201H | 16 |  | MVI | D,3 | ;Loading D with length of substring to use as a counter
4202H | 21 |  | LXI | H,9100H | ;Address of 1st operand
4203H | 06 |  | MVI | B,61H | ;Load B with ASCII Value of ‘a’
4204H | 7E | LOOP: | MOV | A,M | ;Take one character
4205H | B8 |  | CMP | B | ;compare with our required character
4206H | C2 |  | JNZ | RST | ;if both are not same restart process for next character

## Slide 4
MEMORY LOCATION | HEX. CODE | LABEL | MNEMONIC | OPERAND | COMMENT
4207H | 15 |  | DCR | D | ;decrease length of substring to check
4208H | CA |  | JZ | SAVE | ;if whole substring is checked save the answer
4209H | 2C |  | INR | B | ;if substring is not finished move ahead for next character in substring
420AH | 0D | INC: | DCR | C | ;decrease counter of operand
420BH | CA |  | JZ | FIN | ;if operands are finish, end the program
420CH | 2C |  | INX | H | ;otherwise increment address
420DH | 09 |  | JMP | LOOP | ;start from beginning

## Slide 5
MEMORY LOCATION | HEX. CODE | LABEL | MNEMONIC | OPERAND | COMMENT
420EH | 3E | SAVE: | MVI | A,1H | ;save section used when substring is matched
420FH | C3 |  | JMP | DONE | ;go to halt the program
4210H | 3E | FIN: | MVI | A,0H | ;fin section used when substring not found
4211H | 32 | DONE: | STA | 9200H | ;Store result 0 or 1 at 9200H
4212H | 76 |  | HLT |  | ;halt the PC
4213H | 06 | RST: | MVI | B,61H | ;rst section called when B and D need to be reset
4214H | 16 |  | MVI | D,3 | ;reset D
4215H | C3 |  | JMP | INC | ;go to normal program

## Slide 6: Thank You