## Slide 1: Data Transfer Instructions of Microprocessor 8085
Prepared by :
Bijoy Dharaiya 130070107017
Utsav Dodiya 130070107019
Dhruvin Gandhi 130070107022
Guided by :
Prof. S.A.Bakhru
Computer Department,
B. V. M. College, V. V. Nagar.

## Slide 2: Introduction
An instruction is a binary pattern designed inside a microprocessor to perform a specific function.
8085 has 246 instructions.
Each instruction has two parts :
(i)task to be performed, operation code
(ii)data to be operated on, operand
8-bit or 16-bit data, internal register, memory
location, 8-bit or 16-bit address

## Slide 3: Instruction Word Size
The 8085 instruction set is classified into three types according to word size :
(1) 1-byte instruction
- opcode and operand in same byte
(2) 2-byte instruction
- one byte opcode, second byte operand
(3) 3-byte instruction
- one byte opcode, second and third operand

## Slide 4: Classification of Instruction set
There are 5 categories of instruction set,
(1) Data Transfer Instruction,
(2) Arithmetic Instructions,
(3) Logical Instructions,
(4) Branching Instructions,
(5) Control Instructions,

## Slide 5: Data Transfer Operation
The operation copies data from a location called a source to another location, called a destination, without modifying the contents of the source.
The term data transfer is used for copying function.

## Slide 6: Data Transfer Instructions
NO. | Mnemonics | Example | Operation
1 | MVI R, 8-bit | MVI B, 4FH | Load 8-bit data in R
2 | MOV Rd, Rs | MOV A, B | Copy data from source Rs to destination Rd, Rd and Rs can be replaced by memory address M specified by HL register
3 | LXI Rp,16-bit | LXI B, 2050H | Load 16-bit number in Rp
4 | OUT 8-bit | OUT 01H | Send data byte from Accumulator to output device
5 | IN 8-bit | IN 07H | Accept data byte from input device and place it in accumulator
6 | LDA 16-bit | LDA 2050H | Copy data byte into A from memory by 16-bit address
7 | STA 16-bit | STA 2070H | Copy data byte from A into memory by 16-bit address
8 | LDAX Rp | LDAX B | Copy data byte into A from memory by address in Rp
9 | STAX Rp | STAX D | Copy data byte from A into memory by address in Rp

## Slide 7: MOV Instruction
Move
1-byte instruction
Mnemonics:
  MOV Rd, Rs
  MOV M, Rs
  MOV Rd, M
This instruction copies the contents of the source register into the destination register.
The contents of the source register are not altered.
Example: MOV A,B or MOV M,B or MOV C,M

## Slide 8
A | 20 | B | 20
A |  |  | 
B | 30 | C | 
D |  | E | 
H | 20 | L | 50
A |  | B | 20
BEFORE EXECUTION
AFTER EXECUTION
MOV A,B
A |  |  | 
B | 30 | C | 
D |  | E | 
H | 20 | L | 50
A |  |  | 
B |  | C | 
D |  | E | 
H | 20 | L | 50
A |  |  | 
B |  | C | 40
D |  | E | 
H | 20 | L | 50
MOV M,B
MOV C,M
40
40
30
2050H
2050H

## Slide 9: MVI Instruction
Move immediate
2-byte instruction
Mnemonics:
  MVI R, Data(8-bit)
  MVI M, Data(8-bit)
The 8-bit immediate data is stored in the destination register (R) or memory (M), R is general purpose 8 bit register such as A,B,C,D,E,H and L.
Example: MVI B, 60H or MVI M, 40H

## Slide 10
A |  |  | 
B |  | C | 
D |  | E | 
H |  | L | 
A |  |  | 
B | 60 | C | 
D |  | E | 
H |  | L | 
AFTER EXECUTION
BEFORE EXECUTION
MVI B,60H
40
M=2050H
2051H
204FH
204FH
M=2050H
2051H
MVI M,40H
BEFORE EXECUTION
AFTER EXECUTION

## Slide 11: LDA Instruction
Load accumulator
3-byte instruction
Mnemonic:
LDA 16-bit address
The contents of a memory location, specified by a 16-bit address in the operand, are copied to the accumulator (A).
The contents of the source are not altered.
Example: LDA 2000H

## Slide 12
A | 
30
A | 30
30
AFTER EXECUTION
BEFORE EXECUTION
LDA 2000H
2000H
2000H

## Slide 13: STA Instruction
Store into accumulator
3-byte instruction
Mnemonics:
STA 16-bit address
The contents of accumulator are copied into the memory location i.e. address specified by the operand in the instruction.
Example: STA 2000 H

## Slide 14
A | 50
A | 50
50
AFTER EXECUTION
BEFORE EXECUTION
STA 2000H
2000H
2000H

## Slide 15
Thank You