## Slide 1: BIRLA VISHWAKARMA MAHAVIDYALAYA
Subject : Microprocessor and Interfacing
Guided By : S. A. Bakhru
Prepared By :
Anjali Gohel (130070107023)
Khushbu Mistry (130070107028)
Priti Mistry (130070107032)
Data Transfer and Rotate Instructions

## Slide 2: What is instruction?
An instruction is a binary pattern designed inside a microprocessor to perform a specific function.
The entire group of instructions, called instruction set, determines what functions the microprocessor can perform.
8085 has 246 instructions.
Each instruction is represented by an 8-bit binary value.

## Slide 3: Classification of instruction Set
There are 5 Types,
(1) Data Transfer Instruction,
(2) Arithmetic Instructions,
(3) Logical Instructions,
(4) Branching Instructions,
(5) Control Instructions,

## Slide 4: Data Transfer Instruction
These instructions move data between registers, or between memory and register.
These instruction copy data from source to destination.
While coping, the contents of source are not modified.

## Slide 5: Data Transfer Instructions
Opcode | Operand | Bytes | M-cycles | T-states | Types of M-cycle | Flags affected | Addressing mode
MOV | Rd, Rs | 1 | 1 | 4 | F | No flags are affected | Register direct
MOV | M,Rs Rd, M |  | 2 | 7 | F,R | No flags are affected | Register indirect Register direct
MVI | Reg., data | 2 | 2 | 7 | F,R | No flags are affected | Immediate
MVI | Mem., data | 2 | 3 | 10 |  | No flags are affected | Register indirect

## Slide 6
Opcode | Operand | Bytes | M-cycles | T-states | Types of M-cycle | Flags affected | Addressing mode
LXI | REG. pair, 16-bit data | 3 | 3 | 10 |  | No flags are affected | Immediate
LDA | 16 bit address | 1 | 2 | 7 | F,R | No flags are affected | Direct
STA | 16 bit | 3 | 4 | 13 |  | No flags are affected | direct
LDAX | B/D reg. pair | 1 | 2 | 7 | F,R | No flags are affected | Register indirect
STAX | B/D reg. pair | 1 | 2 | 7 | F,R | No flags are affected | Register indirect

## Slide 7
Opcode | Operand | Bytes | M-cycles | T-states | Types of M-cycle | Flags affected | Addressing mode
LHLD | 16 bit address | 3 | 5 | 16 |  | No flags are affected | Direct
SHLD | 16 bit address | 3 | 5 | 16 |  | No flags are affected | Direct
XCHG | none | 1 | 1 | 4 | F | No flags are affected | Register direct

## Slide 8: Rotate Instructions
INSTRUCTION | Operand | Bytes | M-Cycles | T-states | Hex code | Types of M-Cycles | Flags Affected | Addressing Mode
RLC | None | 1 | 1 | 4 | 1F | F | CY (D7) | Implied
RRC | None | 1 | 1 | 4 | 0F | F | CY(D0) | Implied
RAL | None | 1 | 1 | 4 | 17 | F | CY (D7) | Implied
RAR | None | 1 | 1 | 4 | 1F | F | CY(D0) | Implied

## Slide 9: RLC : Rotate accumulator left
Each binary bit of the accumulator is rotated left by one position.
Bit D7 is placed in the position of D0 as well as in the Carry flag.
CY is modified according to bit D7.
S, AC, Z, P are not affected.
Example
Instruction: RLC Hex code:07

## Slide 10
B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
CY
Before Execution
B6 | B5 | B4 | B3 | B2 | B1 | B0 | B7
B7
After Execution

## Slide 11: RAL : Rotate accumulator left through carry
Each binary bit of the accumulator is rotated left by one position through the Carry flag.
Bit D7 is placed in the Carry flag, and the Carry flag is placed in the least significant position D0.
CY is modified according to bit D7. S, AC, Z, P are not affected.
Example:
Instruction: RAL Hex code:17

## Slide 12
B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
CY
B6 | B5 | B4 | B3 | B2 | B1 | B0 | CY
B7
Before Execution
After execution

## Slide 13: RRC : Rotate Accumulator Right
Each binary bit of the accumulator is rotated right by one position.
Bit D0 is placed in the position of D7 as well as in the Carry flag.
CY is modified according to bit D0.
S, AC, Z, P are not affected.
Example:
Instruction: RLC Hex code:0F

## Slide 14
B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
B0 | B7 | B6 | B5 | B4 | B3 | B2 | B1
CY
B0
Before Execution
After Execution

## Slide 15: RAR : Rotate Accumulator right through Carry
Each binary bit of the accumulator is rotated right by one position through the Carry flag.
Bit D0 is placed in the Carry flag, and the Carry flag is placed in the most significant position D7.
CY is modified according to bit D0.
S, AC, Z, P are not affected.
Example:
Instruction: RAR Hex code:1F

## Slide 16
B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0
CY
CY
Before Execution
After Execution

## Slide 17: Fetch Machine Cycle

## Slide 18: Read Machine Cycle

## Slide 19: Write Machine Cycle

## Slide 20: Timing Diagram for STA 526AH Instruction